ME 346: Heat Transfer
ME 346: Heat Transfer
Lecture: Conduction-Introduction
Date: 3 Aug
Instructor: Ankit Jain

---
Recap from Previous Lecture
Refs:
Incropera, Dewitt, Bergman, lavine
Cengel & Ghajar
Recap from Previous Lecture
Transport of energy due to temperature gradient in material
Due to random atomic/molecular motion
Fourier’s law: phenomenological [cannot be derived; from observations]
{𝑞} ^ {”} ∝ {𝑑𝑇} over {𝑑𝑥}
𝑘 : characteristic of a wall material
{𝑞} ^ {”} =− 𝑘 {𝑑𝑇} over {𝑑𝑥}

---
Fourier Law: From Observations
Fourier Law: From Observations
{𝑞} rsub {𝑥} ∝ 𝐴 {ΔT} over {Δ 𝑥}
limit Δ 𝑥 → 0
{𝑞} rsub {𝑥} rsup {”} = {{𝑞} rsub {𝑥}} over {𝐴} = − 𝑘 {dT} over {d 𝑥}
{𝑞} rsub {𝑥} = − 𝑘 𝐴 {ΔT} over {Δ 𝑥}
 because heat-flows in the direction of decreasing temperature

---
Fourier Law: Generalized Form
Fourier Law: Generalized Form
{𝑞} ^ {”} =− 𝑘 𝛻 𝑇
T is a temperature field: T(x,y,z)
gradient operator
Cartesian Coordinates:
𝛻 =( widehat {𝒊} {𝜕} over {𝜕 𝑥} + widehat {𝒋} {𝜕} over {𝜕 𝑦} + widehat {𝒌} {𝜕} over {𝜕 𝑧} )
Isotropic material:

---
Fourier Law: Generalized Form (2)
Fourier Law: Generalized Form
{𝑞} ^ {”} =− 𝑘 𝛻 𝑇
T is a temperature field: T(x,y,z)
gradient operator
Cylindrical Coordinates:
𝛻 =( widehat {𝒓} {𝜕} over {𝜕 𝑟} + widehat {𝝓} {𝜕} over {𝑟 𝜕 ∅} + widehat {𝒛} {𝜕} over {𝜕 𝑧} )

---
Fourier Law: Generalized Form (3)
Fourier Law: Generalized Form
{𝑞} ^ {”} =− 𝑘 𝛻 𝑇
T is a temperature field: T(x,y,z)
gradient operator
Spherical Coordinates:
𝛻 =( widehat {𝑟} {𝜕} over {𝜕 𝑟} + widehat {Θ} {𝜕} over {𝑟 𝜕 Θ} + widehat {𝜙} {𝜕} over {𝑟 sin 𝛩𝜕 ∅} )

---
Thermal Conductivity
Thermal Conductivity
Thermal Conductivity: Measure of how fast heat will flow in a material
{𝑘} rsub {𝑥} ≡− {{𝑞} rsub {𝑥} rsup {”}} over {𝜕 𝑇 / 𝜕 𝑥}
Isotropic Material:

---
Thermal Conductivity: Solids
Thermal Conductivity: Solids
Solids:
 electronic contribution (metals/semi-metals)
lattice/atomic-vibrations (phonons) contribution
 heat capacity
mean velocity
 mean free path

---
Thermal Conductivity: Solids-Boundary Effects
Thermal Conductivity: Solids-Boundary Effects
Jain, Yu, and McGaughey, PRB 87 195301 (2013)
{𝑘} rsub {2} < {𝑘} rsub {1}

---
Thermal Conductivity: Fluids and Insulating Systems
Thermal Conductivity: Fluids and Insulating Systems
Fluids:
Large interatomic spacing than solid inefficient heat transfer compared to solid
Insulating Systems:
Composites with voids (often with reflecting coatings)
Voids often evacuated to reduce the conduction part
Thermal k depends on pressure and can reach as little as 0.004 W/mK.

---
Other Thermal Properties
Other Thermal Properties
- specific heat capacity, ()
- density, ()
- Volumetric heat capacity [, : ability of material to store thermal energy
- Thermal Diffusivity:
 [],
ability of material to conduct thermal energy relative to its ability to store thermal energy.

---
Heat Diffusion Equation
Heat Diffusion Equation
Given initial and boundary conditions, identify temperature distribution inside the material domain
  - determine structural integrity under thermal stress, expansion, etc.
  - determine the material thickness for insulating materials
Consider:
Homogenous medium
No-bulk motion
Temperature distribution
Differential volume

---
Heat Diffusion Equation (2)
Heat Diffusion Equation
Heat flux perpendicular to faces , ,
Heat fluxes on the opposite surfaces [using Taylor series]:
Net rate at which heat is entering the control volume:

---
Heat Diffusion Equation (3)
Heat Diffusion Equation
Energy Balance for control volume for time :
 volumetric energy generation rate

---
Heat Diffusion Equation (4)
Heat Diffusion Equation
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = − left ( {𝜕 {𝑞} rsub {𝑥} rsup {”}} over {𝜕 𝑥} + {𝜕 {𝑞} rsub {𝑦} rsup {”}} over {𝜕 𝑦} + {𝜕 {𝑞} rsub {𝑧} rsup {”}} over {𝜕 𝑧} right ) + dot {𝑞}
Using Fourier’s law:
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) + {𝜕} over {𝜕 𝑦} left (𝑘 {𝜕 𝑇} over {𝜕 𝑦} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞}

---
Heat Diffusion Equation (5)
Heat Diffusion Equation
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) + {𝜕} over {𝜕 𝑦} left (𝑘 {𝜕 𝑇} over {𝜕 𝑦} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞}
Special Cases:
Constant
Steady-state:
Steady-state, no-heat generation, one-dimensional conduction:
𝛼 = {𝑘} over {𝜌 {𝑐} rsub {𝑝}}
{𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) + {𝜕} over {𝜕 𝑦} left (𝑘 {𝜕 𝑇} over {𝜕 𝑦} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞} =0
{𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) =0

---
Heat Diffusion Equation: Cylindrical Coordinates
Heat Diffusion Equation: Cylindrical Coordinates
Consider:
Homogenous medium
No-bulk motion
Temperature distribution
Differential volume
Heat entering on the opposite surfaces [using Taylor series]:
Net rate at which heat is entering the control volume:
ME 346: Heat Transfer, Ankit Jain

---
Heat Diffusion Equation: Cylindrical Coordinates (2)
Heat Diffusion Equation: Cylindrical Coordinates
Energy Balance for control volume for time :
ME 346: Heat Transfer, Ankit Jain

---
Heat Diffusion Equation: Cylindrical Coordinates (3)
Heat Diffusion Equation: Cylindrical Coordinates
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} 𝑟𝑑𝑟𝑑 𝜃 𝑑𝑧𝑑𝑡 =− left ({𝜕 {𝑞} rsub {𝑟}} over {𝜕 𝑟} 𝑑𝑟 + {𝜕 {𝑞} rsub {𝜙}} over {𝜕𝜙} 𝑑 𝜙 + {𝜕 {𝑞} rsub {𝑧}} over {𝜕 𝑧} 𝑑𝑧 right ) 𝑑𝑡 + dot {𝑞} 𝑟𝑑𝑟𝑑 𝜃 𝑑𝑧𝑑𝑡
Using Fourier’s law:
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {1} over {𝑟} {𝜕} over {𝜕 𝑟} left (𝑘𝑟 {𝜕 𝑇} over {𝜕 𝑟} right ) + {1} over {𝑟} {𝜕} over {𝜕𝜙} left (𝑘 {1} over {𝑟} {𝜕 𝑇} over {𝜕𝜙} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞}
ME 346: Heat Transfer, Ankit Jain

---
Heat Diffusion Equation: Spherical Coordinates
Heat Diffusion Equation: Spherical Coordinates
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {1} over {{𝑟} ^ {2}} {𝜕} over {𝜕 𝑟} left (𝑘 {𝑟} ^ {2} {𝜕 𝑇} over {𝜕 𝑟} right ) + {1} over {{𝑟} ^ {2} {sin} ^ {2} {𝜃}} {𝜕} over {𝜕𝜙} left (𝑘 {𝜕 𝑇} over {𝜕𝜙} right ) + {1} over {{𝑟} ^ {2} sin {𝜃}} {𝜕} over {𝜕 𝜃} left (𝑘 sin {𝜃} {𝜕 𝑇} over {𝜕 𝜃} right ) + dot {𝑞}
ME 346: Heat Transfer, Ankit Jain

---
Boundary Conditions
Boundary Conditions
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) + {𝜕} over {𝜕 𝑦} left (𝑘 {𝜕 𝑇} over {𝜕 𝑦} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞}
- Second order in spatial coordinates two boundary conditions for each spatial coordinate
- first order in time one boundary condition in time [known as initial condition]

---
Boundary Conditions (2)
Boundary Conditions
Constant Temperature/ Dirichlet/ Type-I
Constant heat-flux/ Neumann/ Type-II
− 𝑘 {𝑑𝑇} over {𝑑𝑥} {left none right rline} rsub {𝑥 =0 } = {𝑞} rsub {𝑠} rsup {”}
𝑇 left (0, 𝑡 right ) = {𝑇} rsub {𝑠}
melting solid/
boiling liquid
bonding with heater
Convection heat flux/ Type-III
Special Case:
adiabatic
− 𝑘 {𝑑𝑇} over {𝑑𝑥} {left none right rline} rsub {𝑥 =0} = h ( {𝑇} rsub {∞} − 𝑇 (0, 𝑡 ))

---
Problem: Consider a large plane wall of thickness , thermal conductivity and surface area . The two sides of the wall are maintained at constant temperatures and Determine the variation of temperature within the wall under the steady-state conditions.
Schematic:
2 𝐿 𝑥 {𝑇} rsub {1} {𝑇} rsub {2}

---
Known: Surface temperatures, , wall-thickness.
Unknown: distribution inside the wall
Assumptions:
- Constant material properties
- One-dimensional heat transport
- No heat-generation
- Steady-state conditions
Analysis:
{𝑇} rsub {2}
{𝑇} rsub {1}
Heat Diffusion Equation:
𝜌 {𝑐} rsub {𝑝} {𝜕 𝑇} over {𝜕 𝑡} = {𝜕} over {𝜕 𝑥} left (𝑘 {𝜕 𝑇} over {𝜕 𝑥} right ) + {𝜕} over {𝜕 𝑦} left (𝑘 {𝜕 𝑇} over {𝜕 𝑦} right ) + {𝜕} over {𝜕 𝑧} left (𝑘 {𝜕 𝑇} over {𝜕 𝑧} right ) + dot {𝑞}
𝑥
2 𝐿
{{𝑑} ^ {2} 𝑇} over {𝑑 {𝑥} ^ {2}} =0
→ {𝑑𝑇} over {𝑑𝑥} = {𝐶} rsub {1} → 𝑇 ( 𝑥 )= {𝐶} rsub {1} 𝑥 + {𝐶} rsub {2}

---
𝑇 ( 𝑥 )= {𝐶} rsub {1} 𝑥 + {𝐶} rsub {2}
Boundary Conditions:
→ {𝐶} rsub {2} = {{𝑇} rsub {1} + {𝑇} rsub {2}} over {2} {𝐶} rsub {1} = {( {𝑇} rsub {2} − {𝑇} rsub {1} )} over {2 𝐿}
{𝑇} rsub {1}
{𝑇} rsub {2}
𝑇 left (𝑥 right ) = {( {𝑇} rsub {2} − {𝑇} rsub {1} )} over {2 𝐿} 𝑥 + {{𝑇} rsub {1} + {𝑇} rsub {2}} over {2}
𝑥
2 𝐿
Q: Could we get to this linear profile without starting with the Diffusion Eqn.?
Q: What if is a function of ?

---
Q: What if surface are equal but there is a heat generation inside the wall?
Heat Diffusion Equation:
𝑘 {{𝑑} ^ {2} 𝑇} over {𝑑 {𝑥} ^ {2}} + dot {𝑞} =0
{𝑑𝑇} over {𝑑𝑥} =− {dot {𝑞}} over {𝑘} 𝑥 + {𝐶} rsub {1} → 𝑇 =− {dot {𝑞}} over {𝑘} {{𝑥} ^ {2}} over {2} + {𝐶} rsub {1} 𝑥 + {𝐶} rsub {2}
Boundary Conditions:
{𝑇} rsub {1}
{𝑇} rsub {1}
𝑇 left (− 𝐿 right ) = {𝑇} rsub {1} 𝑇 left (𝐿 right ) = {𝑇} rsub {1}
𝑥
Q: What about heat flux Could we something about it?
Q: Where is inside the wall?
2 𝐿

---
 Q: What if we have a long hollow cylinder without any internal heat generation and surfaces maintained at a constant . Under steady-state, would temperature profile be linear?
{𝑇} rsub {2}
{𝑇} rsub {1}
For sphere?

---
© Ankit Jain
All rights reserved.
You may not make copies or disseminate this material in any form without my express permission.